## Slide 1: Spare Register Aware Prefetching for Graph Algorithms on GPUs
Nagesh B Lakshminarayana
Hyesoon Kim

## Slide 2: Graph Algorithms
A rich set of applications and domains would benefit from speeding up the processing of graphs
Web Search
Networks
Data Analytics
Network Security
Chip Design
Bioinformatics

## Slide 3: Speeding Up Graph Algorithms with GPUs
GPUs have been used to speed up many applications
  They provide high throughput and memory bandwidth and are power and energy efficient
Recently, there have been efforts to speed up graph algorithms using GPUs
  Parallel graph algorithms have been implemented to take advantage of the capabilities of GPU

## Slide 4: Efficient Graph Algorithms on GPUs - Challenge
Data dependent memory accesses
  Uncoalesced accesses and memory divergence
  Idle cores due to inability to hide memory access latency completely

## Slide 5: Potential Solution: Prefetching for Graph Algorithms
Prefetch data-dependent memory accesses found commonly in graph algorithms

## Slide 6: Effective Prefetching for Graph Algorithms - Challenges
Identifying the pattern to be prefetched
Prefetching can be less effective due to eviction of prefetched data from cache
  Large number of threads and small cache space per thread can cause eviction of prefetched data
  Due to evictions additional accesses to lower levels of memory hierarchy are required, this could degrade performance
Prefetching can be more effective by using spare registers

## Slide 7: Spare Registers in GPUs
CPUs use all available registers; GPUs may have unused registers
RF
RF
RF
CPU
GPU

## Slide 8: Spare Registers in GPUs
Considerable spare registers are often available
  Threads are allocated to GPU cores at thread block granularity
  Multiple resources must be available to allocate a new thread block
thread
thread
thread
thread
thread
thread
thread
thread
thread
RF
RF
RF
thread block
thread block
thread block
Unused
thread block
thread block
Unused

thread block
thread block
Insufficient registers for
additional thread block
Other resource bottlenecks
prevent further thread allocation
Threads are allocated at
thread block granularity

## Slide 9: Spare Registers in GPUs
Fraction of unused register space out of a 128KB register file
Spare registers can be utilized by threads already assigned
Chart: Fraction of unused register space
| H-BFS | H-SSSP | H-MST | LS-BFS | LS-SSSP | LS-MST | STCON | CLR | MIS
Unused Register Space | 0.29688 | 0.20312 | 0.34375 | 0.40625 | 0.3125 | 0.59375 | 0.28125 | 0.4375 | 0.4375

## Slide 10: Solution: Prefetching for Graph Algorithms
Prefetch a data-dependent memory access pattern found commonly in graph algorithms
Use spare registers to make prefetches more effective
RF
thread block
thread block
Unused
thread block
thread block

## Slide 11: Outline
Introduction and Motivation
SRAP: Spare Register Aware Prefetching
Evaluation
Conclusion

## Slide 12: SRAP – Idea
Prefetch a data dependent access pattern commonly found in graph algorithms
Use spare registers to hold prefetched data
  Prefetched data is inserted into cache as well
  Overwrite spare register only after prefetched data has been used; prefetched data is available in registers even if it is evicted from cache

## Slide 13: Background – Graph Representation on GPUs
Compact Adjacency List representation is used
Graph G(V, E) is represented by two arrays – Va (vertex list) and Ea (edge list)
  There could be additional arrays for different node and edge attributes
Vertex list size is O(#vertices), edge list size is O(#edges)

## Slide 14: Background – Graph Representation
0
1
2
3
4
Edge list
0
1
2
3
4
5
6
7
8
9
Ea
#vertices = 5
#edges = 5
0
1
2
3
4
Vertex list
Va
1
3
2
0
3
4
0
1
0
1
0
3
6
7
9
0
1
3
2
1
0
3
4
0
1
0
0
0
Vertex attribute list
0
1
2
3
4
0
0
Vertex id
Index in Ea where edges
for vertex start
Neighbor
Ea index
1
3
Vertex id

## Slide 15: SRAP – Target Access Pattern
Neighbor list iteration
  Access neighboring vertex and then attribute(s) of neighbor
Processing vertex 1
0
3
6
7
9
Vertex list
0
1
2
3
4
Edge list
1
3
2
0
3
4
0
1
0
1
0
1
2
3
4
5
6
7
8
9
0
1
0
0
0
Vertex attribute list
0
1
2
3
4
3
0
3
4
0
0
3
0
4
0
1
3
0
3
4

## Slide 16: SRAP – Example with Target Access Pattern
Skeleton code from kernel which expands BFS tree
  Each thread is assigned one vertex
    If vertex is active, iterate the neighbor list of that vertex
    For each neighbor examine whether neighbor has already been visited
Attribute-load is dependent on neighbor-load
//neighbor list begins at “start” and ends at “(end - 1)”
for(int i = start; i < end; ++i) {
int id = g_graph_edges[i];
bool visited = g_graph_visited[id];
if(!visited) {
…
}
}
Load neighbor
Load neighbor attribute
id = g_graph_edges[i];
visited = g_graph_visited[id];
id
id

## Slide 17: SRAP – BFS Example
for(int i = start; i < end; ++i) {
int id = g_graph_edges[i];
bool visited = g_graph_visited[id];
if(!visited) {
…
}
}
N-Load
A-Load
Cache block
N-Load
id1
id2
id0
Cache block
A-Load
visited0
visited1
visited2
Cache block
Cache block
…
…

## Slide 18: SRAP – Prefetching Target Access Pattern
N-Load is independent and strided, and A-Load is dependent on N-Load and is random
Prefetching only N-Load would not be very beneficial
  N-Load has a very small stride and would access the same cache block most of the time
Prefetching A-Load would be more beneficial
  To prefetch A-Load we have to prefetch N-Load
for(int i = start; i < end; ++i) {
int id = g_graph_edges[i];
bool visited = g_graph_visited[id];
if(!visited) {
…
}
}
N-Load
A-Load

## Slide 19: SRAP – Prefetching for Graph Algorithms
Prefetch both N-Load and A-Load
Use tag based mechanism in hardware for identifying target loads
  One set for identifying the access patterns of loads
  Another set for detecting dependencies between loads
Enhance pipeline
  Inject instructions into pipeline to prefetch into spare registers
  Manage available spare registers
Compiler assisted mechanism and mechanism with dynamic prefetch distance in paper

## Slide 20: SRAP – Inserting Prefetches
Example Loop with identified access pattern
  Two loads into r2 and r3, second load dependent on first load
  First load has a stride of 4
loop: …
…
ld r2, [r1]
add r3, r0, r2
ld r4, [r3]
…
@p2 bra loop
N-Load
A-Load
A-Load address calculation
ld r2, [r1]
add r3, r0, r2
ld r4, [r3]
r2
r2
r3
r3

## Slide 21: SRAP – Inserting Prefetches
Instruction stream with no prefetching and with SRAP
No prefetching
iterN …
ld r2, [r1]
add r3, r0, r2
ld r4, [r3]
…
@p2 bra loop
iterN+1 …
ld r2, [r1]
add r3, r0, r2
ld r4, [r3]
…
@p2 bra loop
N-Load
A-Load
N-Load
A-Load
iterN …
ld r2, [r1]
add r3, r0, r2
ld r4, [r3]
…
@p2 bra loop
N-Load
A-Load
iterN …
ld r2, [r1]
ld spare1, [r1+4]
add r3, r0, r2
ld r4, [r3]
…
@p2 bra loop
N-Load
A-Load
N-Prefetch
iterN …
ld r2, [r1]
ld spare1, [r1+4]
add r3, r0, r2
ld r4, [r3]
add spare2, r0, spare1
ld spare2, [spare2]
…
@p2 bra loop
N-Load
A-Load
N-Prefetch
A-Prefetch
iterN …
ld r2, [r1]
ld spare1, [r1+4]
add r3, r0, r2
ld r4, [r3]
add spare2, r0, spare1
ld spare2, [spare2]
…
@p2 bra loop
iterN+1 …
ld r2, [r1]
add r3, r0, r2
ld r4, [r3]
…
@p2 bra loop
N-Load
A-Load
N-Prefetch
A-Prefetch
N-Load
A-Load
iterN …
ld r2, [r1]
ld spare1, [r1+4]
add r3, r0, r2
ld r4, [r3]
add spare2, r0, spare1
ld spare2, [spare2]
…
@p2 bra loop
iterN+1 …
mov r2, spare1
add r3, r0, r2
ld r4, [r3]
…
@p2 bra loop
N-Load
A-Load
N-Prefetch
A-Prefetch
Use N-Prefetch
A-Load
iterN …
ld r2, [r1]
ld spare1, [r1+4]
add r3, r0, r2
ld r4, [r3]
add spare2, r0, spare1
ld spare2, [spare2]
…
@p2 bra loop
iterN+1 …
mov r2, spare1
ld spare1, [r1+4]
add r3, r0, r2
ld r4, [r3]
…
@p2 bra loop
N-Load
A-Load
N-Prefetch
A-Prefetch
Use N-Prefetch
N-Prefetch
A-Load
iterN …
ld r2, [r1]
ld spare1, [r1+4]
add r3, r0, r2
ld r4, [r3]
add spare2, r0, spare1
ld spare2, [spare2]
…
@p2 bra loop
iterN+1 …
mov r2, spare1
ld spare1, [r1+4]
add r3, r0, r2
mov r4, spare2
…
@p2 bra loop
N-Load
A-Load
N-Prefetch
A-Prefetch
Use N-Prefetch
N-Prefetch
Use A-Prefetch
iterN …
ld r2, [r1]
ld spare1, [r1+4]
add r3, r0, r2
ld r4, [r3]
add spare2, r0, spare1
ld spare2, [spare2]
…
@p2 bra loop
iterN+1 …
mov r2, spare1
ld spare1, [r1+4]
add r3, r0, r2
mov r4, spare2
add spare2, r0, spare1
ld spare2, [spare2]
…
@p2 bra loop
N-Load
A-Load
N-Prefetch
A-Prefetch
Use N-Prefetch
N-Prefetch
Use A-Prefetch
A-Prefetch
SRAP
iterN …
ld r2, [r1]
ld spare1, [r1+4]
add r3, r0, r2
ld r4, [r3]
add spare2, r0, spare1
ld spare2, [spare2]
…
@p2 bra loop
iterN+1 …
mov r2, spare1
ld spare1, [r1+4]
add r3, r0, r2
mov r4, spare2
add spare2, r0, spare1
ld spare2, [spare2]
…
@p2 bra loop
N-Load
A-Load
N-Prefetch
A-Prefetch
Use N-Prefetch
N-Prefetch
Use A-Prefetch
A-Prefetch

## Slide 22: Outline
Introduction and Motivation
SRAP: Spare Register Aware Prefetching
Evaluation
Conclusion

## Slide 23: Evaluation Methodology
MacSim Simulator
  Trace-driven, cycle-level simulator
Simulate GTX580 (Fermi) GPU
Evaluate kernels from 9 graph algorithms implementations
  IIIT-Hyd, LonestarGPU, some implemented based on previous work
Comparison against Stride, Stream and GHB prefetchers for 3 different inputs
  Since algorithms are iterative kernels are invoked multiple times for each input
Results with prefetch distance of 1 shown, other results (compiler-assisted SRAP, SRAP with dynamic prefetch distance) in paper

## Slide 24: IPC Improvements
Since algorithms are iterative, each kernel is invoked multiple times for a given input
SRAP for all kernels and all inputs – 8%avg and 45%max
Chart: IPC relative to baseline
| H-BFS | LS-MST | CLR | MIS | H-MST | ST-CON | H-SSSP | LS-BFS | LS-SSSP | All Kernels | Harmonic Mean across multiple invocations for different inputs | HMean
Stride | 0.99986 | 1 | 0.99921 | 1.0007 | 1 | 1.0082 | 0.99979 | 0.99727 | 0.99816 | 1
Stream | 0.95016 | 0.99123 | 0.96304 | 0.94921 | 1 | 0.99468 | 0.9866 | 0.9863 | 0.98695 | 0.97
GHB | 1.0019 | 0.99123 | 0.99574 | 0.99766 | 1 | 1.0239 | 1.0065 | 1.0012 | 1.0009 | 1
SRAP | 1.1171 | 1.2019 | 1.1639 | 1.1197 | 1.0248 | 1.0389 | 1.0071 | 1.0357 | 1.0276 | 1.08
No benefit with
prior prefetchers
A-Load cannot be prefetched since
it can be updated by other threads
Good benefit with SRAP

## Slide 25: Benefit From Inserting Into Spare Registers
Caching – Similar to SRAP but attribute-loads are inserted into cache only (Results for only H-BFS with one input shown, other results are in the paper)
For H-BFS with r4_2e20 input – SRAP – 9%avg and 17%max, Caching – 5%avg and 17%max
For all kernels and inputs and invocations – SRAP – 8%avg and Caching – 6%avg
Chart: Improvement in IPC over baseline
| Step 5 | Step 6 | Step 7 | Step 8 | Step 9 | Step 10 | Step 11 | Step 12 | Step 13 | HMean | Invocations w/ R4-2e20 input
SRAP | 1.0868 | 1.1118 | 1.1404 | 1.0484 | 1.0179 | 1.0366 | 1.0662 | 1.1678 | 1.1176 | 1.0861
Caching | 1.0909 | 1.1 | 1.1404 | 1.0484 | 0.96429 | 0.89024 | 0.95588 | 1.1711 | 1.1303 | 1.0463
Additional DRAM requests

## Slide 26: Conclusion
For graph algorithms, prefetching can reduce idle cycles due to memory accesses, but
  Graph algorithms have data dependent accesses
  Effectiveness of prefetching is reduced due to eviction of prefetched data from cache
Soln: SRAP – prefetches a data dependent access pattern; uses spare registers to hold prefetched data and eliminates additional memory accesses due to eviction of prefetch data
The best performing variant of SRAP shows a performance improvement of 10% on average and up to 51%

## Slide 27
Thank you!